## Slide 1: REAL TIME OPERATING SYSTEMS
.

## Slide 2: WHAT IS REAL TIME APPLICATIONS?
The real time systems are the system which the correctness of the computation is not only depends upon the logical correctness but depends upon the time which the result is produce.
If the time constraints are not met means the system said to be not a real time operating system.
Examples of real time system applications
  Airbag deployment
  Missile guidance and control system
  Anti brake system

## Slide 3: WHAT IS REAL TIME OPERATING SYSTEM
It's an operating system, which is specially designed for time constraints application and a high degree of reliability.
Example of Real Time Operating System
  FreeRTOS
  VxWorks
  ONX
  INTEGITY

## Slide 4: WHAT IS SCHEDULER?
Scheduler is the key part of an operating system it decides which task are going to get the CPU time next.
There are many type of CPU scheduling policy's are available.
  Pre-emptive scheduling
  Co-operative scheduling.
To start the cpu scheduler we need to call the function called
vTaskStartScheduler()
Scheduler is the combination of architecture specific code and
FreeRTOS Generic Code.

## Slide 5: .
There are three major function which helps the scheduler runs
vportSVChandler()
xportPendSVhandler()
xportSysTickHandler()

## Slide 6: WHAT IS TASK?
Task is the piece of code which is schedulable.
In FreeRTOS to make an toggle led we need to create following things:
  Task creation
  Task implementation
Task creation is create the memory for the toggle led.
Task implementation is place that how we toggle the led.
In FreeRTOS these two functionality is done by API.

## Slide 7: TASK CREATE AND IMPLEMENTING API’S
To creating a task FreeRTOS provides an api called
BaseType_t xTaskCreate( TaskFunction_t pvTaskCode,
const char * const pcname,
unsigned short usStackDepth,
void *pvParameter,
UBaseType_t uxPriority,
TaskHandle_t *pxCreateTask
);
To implement a task FreeRTOS provides an api called
void vaTaskFunction(void * parameter)
{
for(;;)
{
--here the toggle led code we need to write---
}
vTaskDelete(NULL);
}

## Slide 8: This is happened when the task is created?
At first it will allocate memory in a RAM ,for saving our all tasks which we called heap memory ,it is done by macro called
  #define configHEAP_TOTAL_SIZE
And then it will allocate memory for each task the allocation of memory for the task is determined by this arugment of the xTaskcreate(unsigned short usStackDepth).

## Slide 9: WHAT IS IDLE TASK
Idle task is the task which is created by the RTOS scheduler automatically because for at least one task need to run on the CPU
It is assigned to be a very low priority task
It also having some works like deleting the memory allocated on heap section.
It will help use to put the CPU on sleep mode.

## Slide 10: WHAT IS CONTEXT SWITCHING
Context switching is the process of the switching out of one task and switching in another task to the CPU is called context switching.
In RTOS the context switching is taken care by the scheduler.
But the scheduler internally set the bit of pensv interrupt flag, After that the CPU will execute the pensv handler which actually done the context switching.

## Slide 11: WHAT IS TASK STATE?
The state of the task which is determined by the action of that task
At the execution.
There totally 4 action can be done by the task
  Suspend state
  Running state
  Blocking state
  Ready state

## Slide 12: WHAT IS TASK NOTIFICATION?
Task notification is the method in which we can communicate with the other task which are placed in the scheduler.
There are some API’s which is help us to use the task notification
  BaseType_t xTaskNotifyWait(unit32_t ulBitsToClreaOnEntry,Uint32_t ulBitsToClearOnExit,unit32_t *pulNotificationValue,TickType_t xTickToWait);
  BaseType_t xTaskNotify(TaskHandle_t xTaskToNotify,unit32_t ulValue,eNotifyAction eAction);

## Slide 13: HOW WE CAN DELETE THE TASK
Void xTaskDelete(TaskHandle pxTaskToDelete) by using this api we able to delete task from the scheduler.
Note:
xtaskDelete actually make the mark of the task to be delete, the deletion part taken by the idle task.

## Slide 14: D/B TASK PRIORITY AND HARDWARE PRIORITY
Task priority is assigned to the ISR of FreeRTOS and Hardware priority is assigned to the ISR of the hardware.
If the priority assigning to the hardware interrupt means we need to assign the lowest number possible.
If the priority assigning to the task interrupt means we need to assign the highest number possible.
For example:
  We need to calculate the sensor of ultrasonic for every detection of movement, this is considered to a hardware interrupt(lowest number possible).
  The pensv interrupt and systick interrupt are consider to be an task interrupt(highest number possble).

## Slide 15: .
To find the highest number possible and lowest number possible for the priority means we need to look for the
ConfigKERNEK_INTERRUPT_PRIORITY
ConfigMAX_SYSCALL_INTERRUPT_PRIORITY

## Slide 16: WHAT IS HOOK FUNCTION
Hook function are the function which will get when ever the software interrupt are occurs.
To achieve this Hook function, we need to configure the config file of the FreeRTOS.
Type of Hook functions
  Idle task hook function
  RTOS tick hook function
  Dynamic memory allocation fail hook function.
  Stack overflow hook function.

## Slide 17: .

## Slide 18: WHAT IS QUEUE
Queue is the thread safe FIFO buffer, which let the task communicate with each other and avoid race condition.
The sends goes to sleep when the queue is full, the receiver goes to sleep when the queue is empty.
So the CPU cycle is never be wasted.

## Slide 19: HOW TO CREATE THE QUEUE AND SENDING DATA TO QUEUE
xQueueHandle xQueueCreate (unsigned portBASE_TYPE uxQueuelength,
unsigned portBASE_TYPE uxItemSize);
portBASE_TYPE xQueueSendToFront(xQueueHandle xQueue,
const void* pvItemToQueue,
portTickType xTicksToWait);

## Slide 20: HOW TO RECEIVE FROM QUEUE
portBASE_TYPE xQueueReceive (xQueueHandle xQueue,
void *pvbuffer,
portTICKTYPE xTicktowait);
portBASE_TYPE xQueuePeek (xQueueHandle xQueue,
void *pvbuffer,
portTICKTYPE xTicktowait);

## Slide 21: SEMAPHORE
Semaphore is a signalling mechanism which is used to pass the signal from one task to another task without any data.
Semaphore help us to avoid the race condition in the multitasking environments.
Type of semaphore
  Binary semaphore
  Counting semaphore

## Slide 22: SEMAPHORE RELATED API’S
xSemaphoreCreateBinary()
xSemaphoreCreateCounting()
xSemaphoreGive()
xSemaphoreGiveFromISR()
xSemaphoreTake()

## Slide 23: WHAT IS MUTUAL EXCLUSION
Mutex is a kernel synchronization primitive implementing ownership semantics and priority inheritance protocol to prevent priority inversion while ensuring mutual exclusion on shared resources in a pre-emptive multitasking environment.

## Slide 24: MUTEX REALATED API’S
SemaphoreHandle_t xSemaphoreCreateMutex(void);
BaseType_t xSemaphoreGive(
SemaphoreHandle_t xSemaphore // mutex handle );
void vSemaphoreDelete(
SemaphoreHandle_t xSemaphore // mutex handle
);
BaseType_t xSemaphoreTake(
SemaphoreHandle_t xSemaphore, // mutex handle
TickType_t xTicksToWait // timeout
        );